## Slide 1: Supporting Procedures in Computer H/W
Nested procedure example
Q) Let’s tackle a recursive procedure that calculates factorial: long long int fact (long ling int n)
{
if (n < 1) return (1);
else return (n * fact (n – 1) );
} What is the RISC-V assembly code? The parameter variable n corresponds to the argument register x10.

## Slide 2: Supporting Procedures in Computer H/W
Nested procedure example
Allocate and save data into the stack.
n-1 and compare to 0. and branch to the L1 procedure following condition.
n-1 and compare to 0. and branch to the fact procedure following condition.
Load data and multiply n and n-1.
Decrease the stack pointer whenever load the old data.
Terminate the procedure.
Return 1, decrease the stack pointer and terminate the procedure.
fact : addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)

## Slide 3: Supporting Procedures in Computer H/W
Execution example with n=3
Assumption) return address of the procedure call is 8000, and initial stack pointer is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1024
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1024 | 3 | 8000 | - | -

## Slide 4: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | - | -
〮 Decrease sp by 16 to push data of variable “n” (x10) and return address (x1)

## Slide 5: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | - | -
〮 Store return address (x1) into Stack
8000

## Slide 6: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | - | -
〮 Store value of variable “n” (x10) into Stack
8000

## Slide 7: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | 2 | -
〮 x5 = x10 – 1 = 3 – 1 = 2
(x5 = n – 1)
8000

## Slide 8: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | 2 | -
〮 Branch to L1 if x5 (n-1) is greater than 0 (x0) (goto L1 if (n-1) ≥ 0 (or n ≥ 1)
8000

## Slide 9: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 8000 | 2 | -
〮 Calculate x10 = x10 – 1 = 3 – 1 = 2 (To get (n-1))
8000

## Slide 10: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 9000 | 2 | -
〮 Jump to fact after store return address into x1 (Assume return address is 9000, in other words, the address of addi x6, x10, 0 is 9000)
8000

## Slide 11: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | 2 | -
8000
992
〮 Decrease sp by 16 to push data of x10 and
x1

## Slide 12: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | 2 | -
8000
9000
992
〮 Store return address saved in x1 into Stack

## Slide 13: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | 2 | -
8000
2
9000
992
〮 Store value saved in x10 into Stack

## Slide 14: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | 1 | -
8000
2
9000
992
〮 x5 = x10 – 1 = 2 – 1 = 1
(x5 = n – 1)

## Slide 15: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | 1 | -
8000
2
9000
992
〮 Branch to L1 if x5 (n-1) is greater than 0 (x0) (goto L1 if (n-1) ≥ 0 (or n ≥ 1)

## Slide 16: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | 1 | -
8000
2
9000
992
〮 Calculate x10 = x10 – 1 = 2 – 1 = 1 (To get (n-1))

## Slide 17: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | 1 | -
8000
2
9000
992
〮 Jump to fact after store return address into x1 (Assume return address is 9000)

## Slide 18: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | 1 | -
8000
2
9000
〮 Decrease sp by 16 to store the value of x10 and
x1
976

## Slide 19: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | 1 | -
8000
2
9000
〮 Store return address saved in x1 into Stack
9000
976

## Slide 20: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | 1 | -
8000
2
9000
〮 Store value saved in x10 into Stack
1
9000
976

## Slide 21: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | 0 | -
8000
2
9000
〮 x5 = x10 – 1 = 1 – 1 = 0
(x5 = n – 1)
1
9000
976

## Slide 22: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | 0 | -
8000
2
9000
〮 Branch to L1 if x5 (n-1) is greater than 0 (x0) (goto L1 if (n-1) ≥ 0 (or n ≥ 1)
1
9000
976

## Slide 23: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 0 | 9000 | 0 | -
8000
2
9000
〮 Calculate x10 = x10 – 1 = 1 – 1 = 0 (To get (n-1))
1
9000
976

## Slide 24: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 0 | 9000 | 0 | -
8000
2
9000
〮 Jump to fact after store return address into x1 (Assume return address is 9000)
1
9000
976

## Slide 25: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 0 | 9000 | 0 | -
8000
2
9000
〮 Decrease sp by 16 to store the value of x10 and
x1
1
9000
960

## Slide 26: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 0 | 9000 | 0 | -
8000
2
9000
〮 Store return address saved in x1 into Stack
1
9000
9000
960

## Slide 27: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 0 | 9000 | 0 | -
8000
2
9000
〮 Store value saved in x10 into Stack
1
9000
0
9000
960

## Slide 28: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 0 | 9000 | -1 | -
8000
2
9000
〮 x5 = x10 – 1 = 0 – 1 = – 1
(x5 = n – 1)
1
9000
0
9000
960

## Slide 29: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 0 | 9000 | -1 | -
8000
2
9000
〮 Branch to L1 if x5 (n-1) is greater than 0 (x0) (goto L1 if (n-1) ≥ 0 (or n ≥ 1)
〮 In this case, not branch
1
9000
0
9000
960

## Slide 30: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 960 | 1 | 9000 | -1 | -
8000
2
9000
〮 Variable n (x10) is less than 1, x10 will have 1
if (n < 1) return (1);
1
9000
0
9000
960

## Slide 31: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | -1 | -
8000
2
9000
〮 Increase sp by 16
1
9000
976

## Slide 32: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | -1 | -
8000
2
9000
〮 Jump to address saved in x1 register
x1 register have return address “9000”
1
9000
976

## Slide 33: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | -1 | 1
8000
2
9000
〮 Copy value of x10 into x6 register
〮 x6 reg will have 1 (x10)
1
9000
976

## Slide 34: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | -1 | 1
8000
2
9000
〮 Load value 1 from Stack to x10 reg
1
9000
976

## Slide 35: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 976 | 1 | 9000 | -1 | 1
8000
2
9000
〮 Load return address from Stack into x1 reg
1
9000
976

## Slide 36: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | -1 | 1
8000
2
9000
992
〮 Increase sp by 16

## Slide 37: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | -1 | 1
8000
2
9000
992
〮 Multiply x10 and x6
The result will be stored into x10 reg x10 = 1*1 = 1

## Slide 38: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | -1 | 1
8000
2
9000
992
〮 Jump to address saved in x1 register
x1 register have return address “9000”

## Slide 39: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 1 | 9000 | -1 | 1
8000
2
9000
992
〮 Copy value of x10 into x6 register
〮 x6 reg will have 1 (x10)

## Slide 40: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | -1 | 1
8000
2
9000
992
〮 Load value 2 from Stack to x10 reg

## Slide 41: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 992 | 2 | 9000 | -1 | 1
8000
2
9000
992
〮 Load return address from Stack into x1 reg

## Slide 42: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 9000 | -1 | 1
8000
〮 Increase sp by 16

## Slide 43: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 9000 | -1 | 1
8000
〮 Multiply x10 and x6
The result will be stored into x10 reg x10 = 2 * 1 = 2

## Slide 44: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 9000 | -1 | 1
8000
〮 Jump to address saved in x1 register
x1 register have return address “9000”

## Slide 45: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 2 | 9000 | -1 | 2
8000
〮 Copy value of x10 into x6 register
〮 x6 reg will have 2 (x10)

## Slide 46: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 9000 | -1 | 2
8000
〮 Load value 3 from Stack to x10 reg

## Slide 47: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1008
3
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1008 | 3 | 8000 | -1 | 2
8000
〮 Load return address from Stack into x1 reg

## Slide 48: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1024
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1024 | 3 | 8000 | -1 | 2
〮 Increase sp by 16

## Slide 49: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1024
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1024 | 6 | 8000 | -1 | 2
〮 Multiply x10 and x6
The result will be stored into x10 reg x10 = 3 * 2 = 6

## Slide 50: Supporting Procedures in Computer H/W
Assume that “n” is 3 & current “sp” is 1024
fact :
addi sp, sp, -16
sd x1, 8(sp)
sd x10, 0(sp)
addi x5, x10, -1 bge x5, x0, L1
addi x10, x0, 1
addi sp, sp, 16
jalr x0, 0(x1)
L1: addi x10, x10, -1
jal x1, fact
addi x6, x10, 0
ld x10, 0(sp)
ld x1, 8(sp)
addi sp, sp, 16
mul x10, x10, x6
jalr x0, 0(x1)
1024
Stack
︙
 | sp | x10 | x1 | x5 | x6
Value | 1024 | 3 | 8000 | -1 | 2
〮 Jump to address saved in x1 register
x1 register have return address “8000” fact(3) finish with result “6”